| Source Activity | Mitigation Measure | PM10 Control Efficiency | Comments | Estimated Cost |
| --- | --- | --- | --- | --- |
| Travel over unpaved roads | Limit maximum speed on unpaved roads to 25 miles per hour. | 44% | Assumes linear relationship between PM10 emissions and vehicle speed and an uncontrolled speed of 45 mph. | ND |
| Travel over unpaved roads | Pave unpaved roads and unpaved parking areas. | 99% | Based on comparison of paved road and unpaved road PM10 emission factors. | $44,100/mile-year (useful life of 25 years) |
| Travel over unpaved roads | Implement watering twice a day for industrial unpaved road. | 55% |  | ND |
| Travel over unpaved roads | Apply chemical dust suppressant annually to unpaved parking areas. | 84% |  | $5,340/acre-year (useful life of 1 year) |

# Footnotes

Unless otherwise noted, information presented in this table is from the following reference:  WRAP Fugitive Dust Handbook, September 7, 2006 (http://www.wrapair.org/forums/dejf/fdh/content/FDHandbook_Rev_06.pdf). ND = No Data.

2003 dollars.